On the basis of Article 63. paragraph 1 of the Law of Public procurement (Official Gazette RS no. 124/12) we publish

The change to the bidding documentation

For the public procurement number 28/15/606006 – Steel mining supports with connecting elements

The changes refer to the number of steel mining supports and connecting elements which are the topic of this public procurement, as well as the dynamics and delivery deadlines. With regards to this the following documents are changed in the bidding documentation no. 5402:

1 ) Instruction to bidders on how to prepare a bid: article 10 (page no. 7) the validity of bids…

“Delivery of steel mining support (positions 1, 2, 3, 4 and 5) is to be made ​​in twelve equal monthly tranches, as follows: I tranche (1/12 contracted quantity for each position) - 30 days after signing the contract,  the remaining eleven tranches at dynamics: circa 1/12 contracted quantity / monthly) -  binding elements (positions 6 and 7) are to be supplied in adequate numbers with each delivery of steel support.”

The said text is changed and should stand as:

The deadline and dynamics of delivery : Delivery of steel mining support (positions 1, 2, 3, 4 and 5) is to be made ​​in six equal monthly tranches, as follows: I tranche (1/6 contracted quantity for each position) - 30 days after signing the contract,  the remaining five tranches at dynamics: circa 1/6 contracted quantity / monthly) -  binding elements (positions 6 and 7) are to be supplied in adequate numbers with each delivery of steel support.

2) The bid form can be found on pages 16/61, 17/61 and 18/61, which read as follows:

| No. | The subject of procurement | Unit | Quantity | Price | Total value |
| --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 |
| 1. | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel bent into the profile Ø 4 m | Frame | 1800 |  |  |
| 2. | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel in bento into the profile about Ø 3.5 m | Frame | 6000 |  |  |
| `3. | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel in the directions of length L = 7,1m | piece | 1 200 |  |  |
| 4. | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel in the directions of length L = 6,4m | piece | 1350 |  |  |
| 5. | Bell-shaped profile weight 28-29 kg, with the following charctheristics -Tensile strength 550 N/mm2 -Moment of resistance minimum Wx=90cm3 -Deliver steel bent as in drawing 1 | Frame | 425 |  |  |
| 6. | Binding elements for steel support appropriate for the bell profile number 1, 2, 3 and 4. | Set | 70500 |  |  |
| 7. | Binding elements for steel support appropriate for the bell profile number 5 | Set | 2550 |  |  |

TOTAL: ___________________

(RSD / EUR)

VAT: _____________________

(RSD / EUR)

PAYMENT: ________________

(RSD / EUR)

The offer is given:

(Circle and enter the data for a), b) or c)

a) independently

b) with a subcontractor

1. _________________________________________________________________________

2. _________________________________________________________________________

_____________________________________________________________________ 3. ____

(State the name and residence of all subcontractors)

v) as a joint offer

1. _________________________________________________________________________

2. _________________________________________________________________________

3. ______________ ___________________________________________________________

(State the name and residence of all bidders of the joint bid)

| Terms of delivery and delivery schedule: | Delivery of steel mining support (positions 1, 2, 3, 4 and 5) is to be made in twelve equal monthly tranches, as follows: I tranche (approximately 1/12 of the contracted quantity for each position) - 30 days after conclusion of the contract, the other eleven tranches at dynamics: approx 1/12 of the contracted quantity / monthly; binding elements (positions 6 and 7) in the appropriate number for each shipment of steel mining support |
| --- | --- |
| Place of delivery and parity | DDP Resavica - central warehouse (Incoterms 2010), |
| The validity of the offery (not less than 60 days): |  |
| Country of origin and name of the manufacturer:  for positions 1, 2, 3. and 4.  for 5. position -for position 6 -for position 7 |  |

The said text is changed and should stand as:

| No. | The subject of procurement | Unit | Quantity | Price | Total value |
| --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 |
| 1. | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel bent into the profile Ø 4 m | Frame | 1116 |  |  |
| 2. | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel in bento into the profile about Ø 3.5 m | Frame | 3360 |  |  |
| `3. | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel in the directions of length L = 7,1m | piece | 780 |  |  |
| 4. | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel in the directions of length L = 6,4m | piece | 876 |  |  |
| 5. | Bell-shaped profile weight 28-29 kg, with the following charctheristics -Tensile strength 550 N/mm2 -Moment of resistance minimum Wx=90cm3 -Deliver steel bent as in drawing 1 | Frame | 425 |  |  |
| 6. | Binding elements for steel support appropriate for the bell profile number 1, 2, 3 and 4. | Set | 42000 |  |  |
| 7. | Binding elements for steel support appropriate for the bell profile number 5 | Set | 2550 |  |  |

TOTAL: ___________________

(RSD / EUR)

VAT: _____________________

(RSD / EUR)

PAYMENT: ________________

(RSD / EUR)

The offer is given:

(Circle and enter the data for a), b) or c)

a) independently

b) with a subcontractor

1. _________________________________________________________________________

2. _________________________________________________________________________

_____________________________________________________________________ 3. ____

(State the name and residence of all subcontractors)

v) as a joint offer

1. _________________________________________________________________________

2. _________________________________________________________________________

3. ______________ ___________________________________________________________

(State the name and residence of all bidders of the joint bid)

| Terms of delivery and delivery schedule: | Delivery of steel mining support (positions 1, 2, 3, 4 and 5) is to be made in six equal monthly tranches, as follows: I tranche (approximately 1/6 of the contracted quantity for each position) - 30 days after conclusion of the contract, the other five tranches at dynamics: approx 1/6 of the contracted quantity / monthly; binding elements (positions 6 and 7) in the appropriate number for each shipment of steel mining support |
| --- | --- |
| Place of delivery and parity | DDP Resavica - central warehouse (Incoterms 2010), |
| The validity of the offery (not less than 60 days): |  |
| Country of origin and name of the manufacturer: for positions 1, 2, 3. and 4.  for 5. position -for position 6 -for position 7 |  |

3) Form cost price structure on pages 35/61 and 36/61, which read as follows:

|  | Unit of measurement | Unit Price without VAT | Unit price with VAT | The VAT rate per unit price | The amount of VAT per unit price | Quantity | The total value excluding VAT | The amount of VAT on the total value | The total value of + VAT |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| Bell-shaped profile, 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel bent into the profile Ø 4 m | Frame |  |  |  |  | 1800 |  |  |  |
| Bell-shaped profile, 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel bent into a profile Ø 3,5 m | Frame |  |  |  |  | 6000 |  |  |  |
| Bell-shaped profile, 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel in directions of length L = 7,1m | Piece |  |  |  |  | 1200 |  |  |  |
| Bell-shaped profile, 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel in directions of length L = 6,4m | Piece |  |  |  |  | 1350 |  |  |  |
| Bell-shaped profile, 28-29 kg/m, with the following characteristics -Tensile strength 550 N/mm2 -Moment of resistance minimum Wx=90cm3 -Deliver steel bent as in the drawing 1 | Frame |  |  |  |  | 425 |  |  |  |
| The binding elements of steel support appropriate for the bell-shaped profile numbered 1, 2, 3 and 4 | Set |  |  |  |  | 70500 |  |  |  |
| The binding elements of steel support appropriate for the bell-shaped profile numbered 5 | Set |  |  |  |  | 2550 |  |  |  |

The said text is changed and should stand as:

|  | Unit of measurement | Unit Price without VAT | Unit price with VAT | The VAT rate per unit price | The amount of VAT per unit price | Quantity | The total value excluding VAT | The amount of VAT on the total value | The total value of + VAT |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| Bell-shaped profile, 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel bent into the profile Ø 4 m | Frame |  |  |  |  | 1116 |  |  |  |
| Bell-shaped profile, 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel bent into a profile Ø 3,5 m | Frame |  |  |  |  | 3360 |  |  |  |
| Bell-shaped profile, 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel in directions of length L = 7,1m | Piece |  |  |  |  | 780 |  |  |  |
| Bell-shaped profile, 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel in directions of length L = 6,4m | Piece |  |  |  |  | 876 |  |  |  |
| Bell-shaped profile, 28-29 kg/m, with the following characteristics -Tensile strength 550 N/mm2 -Moment of resistance minimum Wx=90cm3 -Deliver steel bent as in the drawing 1 | Frame |  |  |  |  | 425 |  |  |  |
| The binding elements of steel support appropriate for the bell-shaped profile numbered 1, 2, 3 and 4 | Set |  |  |  |  | 42000 |  |  |  |
| The binding elements of steel support appropriate for the bell-shaped profile numbered 5 | Set |  |  |  |  | 2550 |  |  |  |

4) Technical specifications and drawungs on pages 47/61 and 48/61, which read as follows:

  - Bell-shaped profile weight 23-24 kg / m, quantity 1800 frames

with the following characteristics:

- Tensile strength 470 N / mm ²

- Moment of resistance  minimum Wx = 68 cm³

- Deliver steel bent into a circular profile Ø 4 m (Drawing no. 3)

  - Bell-shaped profile weight 23-24 kg / m, quantity 6000 frames

with the following characteristics:

- Tensile strength 470 N / mm ²

- Moment of resistance minimum Wx = 68 cm³

- Deliver steel bent into a circular profile Ø 3,5 m (drawing no. 4)

3.    Bell-shaped profile weight 23-24 kg / m,   quantity 1 200 pieces

with the following characteristics

- Tensile strength 470 N / mm ²

- Moment of resistance minimum Wx = 68 cm³

- Deliver steel  in  directions of length L = 7.1 m

4. Bell-shaped profile weight 23-24 kg / m, quantity 1350  pieces

with the following characteristics:

- Tensile strength 470 N / mm ²

- Moment of  resistance minimum Wx = 68 cm³

- Deliver steel  in  directions of length L = 6.4 m

5. Bell-shaped profile weight 28-29 kg / m, quantity 425   pieces

with the following characteristics:

- Tensile strength 550 N / mm ²

- Moment of resistance minimum Wx = 90 cm³

- Deliver steel  in bent as in the drawing No 1

6. Binding elements of steel support, quantity 70 500 sets (drawing no. 2  attached  to technical specifications serves only to clarify the concept of binding elements (connecting devices) for some so far used types of steel mining support).

7. Binding elements of steel support suitable for bell-shaped profile in no. 5., quantity 2 550 sets.

       Steel bell-shaped profiles numbered as 1, 2, 3. and 4. must be made ​​of steel E295 designated EN or appropriate, that is made ​​of steel with the appropriate label depending on the country of origin.

     Steel bell-shaped profiles numbered as 1, 2, 3. and 4. must be made ​​of the same bell profile  with the same designation.

-     Steel bell-shaped profile numbered as 5 must be made of steel DIN21350 according to standard DIN 21350 or another appropriate, that is made of steel with the corresponding designation depending of the country of origin.

      The bidder is required to submit the catalog documentation for the offered steel mining support  by the  manufacturer of steel mining support which he stated in the Bid Form and whose original letter (authorization) of the manufacturer he has submitted as the  requested additional evidence.

       Binding elements  under 6. are delivered in sets consisting of   clamps, stirrups and two nuts and must be appropriate for the bell-shaped profile under  1, 2, 3. and 4, and binding elements under 7. must be appropriate for bell-shaped profile under  5.

       Delivery of steel mining support (positions 1, 2, 3 , 4 and 5) is to be done ​​in twelve equal monthly tranches, as follows: I tranche  (approximately 1/12 of the agreed quantity for each position) - 30 days after the conclusion of the contract, other eleven tranches  at dynamics: approximately 1/12 of the agreed quantity / monthly; binding elements (positions 6 and 7) in the appropriate number for each shipment of steel mining support

       With each delivery of steel mining support  (positions 1, 2, 3, 4 and 5) an attestation (certificate)  issued by the manufacturers is to be submitted as evidence of compliance for the quality of the delivered quantity of steel mining support with a quality characteristics set out in the original letter (authorization)of the manufacturer.

       If during exploitation of the delivered steel mining support a need for checking the quality arises, the purchaser reserves the right to verify the quality at the local authorized institution, by method of random choice, in the presence  of representatives of both the Purchaser and the Bidder

The said text is changed and should stand as:

    - Bell-shaped profile weight 23-24 kg / m, quantity 1116 frames

with the following characteristics:

- Tensile strength 470 N / mm ²

- Moment of resistance  minimum Wx = 68 cm³

- Deliver steel bent into a circular profile Ø 4 m (Drawing no. 3)

    - Bell-shaped profile weight 23-24 kg / m, quantity 3360 frames

with the following characteristics:

- Tensile strength 470 N / mm ²

- Moment of resistance minimum Wx = 68 cm³

- Deliver steel bent into a circular profile Ø 3,5 m (drawing no. 4)

3.    Bell-shaped profile weight 23-24 kg / m,   quantity 780 pieces

with the following characteristics

- Tensile strength 470 N / mm ²

- Moment of resistance minimum Wx = 68 cm³

- Deliver steel  in  directions of length L = 7.1 m

4. Bell-shaped profile weight 23-24 kg / m, quantity 876  pieces

with the following characteristics:

- Tensile strength 470 N / mm ²

- Moment of  resistance minimum Wx = 68 cm³

- Deliver steel  in  directions of length L = 6.4 m

5. Bell-shaped profile weight 28-29 kg / m, quantity 425   pieces

with the following characteristics:

- Tensile strength 550 N / mm ²

- Moment of resistance minimum Wx = 90 cm³

- Deliver steel  in bent as in the drawing No 1

6. Binding elements of steel support, quantity 42000 sets (drawing no. 2  attached  to technical specifications serves only to clarify the concept of binding elements (connecting devices) for some so far used types of steel mining support).

7. Binding elements of steel support suitable for bell-shaped profile in no. 5., quantity 2 550 sets.

       Steel bell-shaped profiles numbered as 1, 2, 3. and 4. must be made ​​of steel E295 designated EN or appropriate, that is made ​​of steel with the appropriate label depending on the country of origin.

     Steel bell-shaped profiles numbered as 1, 2, 3. and 4. must be made ​​of the same bell profile  with the same designation.

-     Steel bell-shaped profile numbered as 5 must be made of steel DIN21350 according to standard DIN 21350 or another appropriate, that is made of steel with the corresponding designation depending of the country of origin.

      The bidder is required to submit the catalog documentation for the offered steel mining support  by the  manufacturer of steel mining support which he stated in the Bid Form and whose original letter (authorization) of the manufacturer he has submitted as the  requested additional evidence.

       Binding elements  under 6. are delivered in sets consisting of   clamps, stirrups and two nuts and must be appropriate for the bell-shaped profile under  1, 2, 3. and 4, and binding elements under 7. must be appropriate for bell-shaped profile under  5.

       Delivery of steel mining support (positions 1, 2, 3 , 4 and 5) is to be done ​​in six equal monthly tranches, as follows: I tranche  (approximately 1/6 of the agreed quantity for each position) - 30 days after the conclusion of the contract, other five tranches  at dynamics: approximately 1/6 of the agreed quantity / monthly; binding elements (positions 6 and 7) in the appropriate number for each shipment of steel mining support

       With each delivery of steel mining support  (positions 1, 2, 3, 4 and 5) an attestation (certificate)  issued by the manufacturers is to be submitted as evidence of compliance for the quality of the delivered quantity of steel mining support with a quality characteristics set out in the original letter (authorization)of the manufacturer.

       If during exploitation of the delivered steel mining support a need for checking the quality arises, the purchaser reserves the right to verify the quality at the local authorized institution, by method of random choice, in the presence  of representatives of both the Purchaser and the Bidder

- Contract model, Article 3., page 55/61 and 56/61,  which read as follows:

The seller is obligated to deliver to Buyer the steel mining support with binding elements to parity DDP (Incoterms 2010) Resavica - central warehouse, all in accordance with  specification and prices set out in the Seller's bid number _____of ______________as follows:

| Item no. | Subject of procurement | Unit | Quantity | Price | The total value |
| --- | --- | --- | --- | --- | --- |
| 1 | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resisyance minimum Wx = 68 cm³ - Deliver steel bent into the profile Ø 4 m | Frame | 1800 |  |  |
| 2 | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel bent into the profile Ø 3.5 m | Frame | 6000 |  |  |
| `3 | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel in directions of length L = 7,1m | piece | 1 200 |  |  |
| 4 | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel in directions of length L = 6,4m | piece | 1350 |  |  |
| `5. | Bell-shaped profile weight 28-29 kg/mm with the following characteristics -Tensile strength 550 N/mm2 -Moment of resistance minimum Wx=90ccm -Deliver steel bent as in drawing 1 | Set | 50 000 |  |  |
| 6 | Binding elements of steel support Appropriate for the bell-shaped profile number 1, 2, 3 and 4 | Set | 70500 |  |  |
| 7 | Binding elements of steel support appropriate for the bell-shaped profile number 5 | Set | 2550 |  |  |

The total value of the contract without VAT is _________________ RSD / EUR.

VAT amounts to _________________ RSD / EUR.

The total value of the contract with the VAT amounts to _________________ RSD / EUR.

Price will be charged equivalent in RSD according to the average exchange rate of the National Bank of Serbia valid at the date of delivery of the goods.

Seller guarantees the immutability of  the price till the final realization of the contract.

Contracting parties recognize in accordance that the agreed price of this article covers all costs  the Seller has in execution of this contract.

The said text is changed and should stand as:

The seller is obligated to deliver to Buyer the steel mining support with binding elements to parity DDP (Incoterms 2010) Resavica - central warehouse, all in accordance with  specification and prices set out in the Seller's bid number _____of ______________as follows:

| Item no. | Subject of procurement | Unit | Quantity | Price | The total value |
| --- | --- | --- | --- | --- | --- |
| 1 | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resisyance minimum Wx = 68 cm³ - Deliver steel bent into the profile Ø 4 m | Frame | 1116 |  |  |
| 2 | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel bent into the profile Ø 3.5 m | Frame | 3360 |  |  |
| `3 | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel in directions of length L = 7,1m | piece | 780 |  |  |
| 4 | Bell-shaped profile weight 23-24 kg / m, with the following characteristics: - Tensile strength 470 N / mm² - Moment of resistance minimum Wx = 68 cm³ - Deliver steel in directions of length L = 6,4m | piece | 876 |  |  |
| `5. | Bell-shaped profile weight 28-29 kg/mm with the following characteristics -Tensile strength 550 N/mm2 -Moment of resistance minimum Wx=90ccm -Deliver steel bent as in drawing 1 | Frame | 425 |  |  |
| 6 | Binding elements of steel support Appropriate for the bell-shaped profile number 1, 2, 3 and 4 | Set | 42000 |  |  |
| 7 | Binding elements of steel support appropriate for the bell-shaped profile number 5 | Set | 2550 |  |  |

The total value of the contract without VAT is _________________ RSD / EUR.

VAT amounts to _________________ RSD / EUR.

The total value of the contract with the VAT amounts to _________________ RSD / EUR.

Price will be charged equivalent in RSD according to the average exchange rate of the National Bank of Serbia valid at the date of delivery of the goods.

Seller guarantees the immutability of  the price till the final realization of the contract.

Contracting parties recognize in accordance that the agreed price of this article covers all costs  the Seller has in execution of this contract.

- Contract model, Article 6, page 57/61, which read as follows:

Seller agrees to deliver the contractual goods-steel mining support (positions 1, 2, 3, 4 and 5 of the contract)  to the Buyer , DDP Resavica- Central warehouse Resavica (Incoterms 2010), in 12 (twelve) equal monthly tranches  (approximately 1/12 contracted quantity for each position), as follows:

1. First tranche – no later within 30 (thirty) days from the day the contract goes into effect;

2. Second tranche-no later that 2 (two) months from the day the contract goes into effect;

3. Third tranche-no later than 3 (three) months from the day the contract goes into effect;

4. Fourtt tranche-no later than 4 (four) months from the day the contract goes into effect;

5. Fifth tranche-no later than 5 (five) months from the day the contract goes into effect;

6. Sixth tranche-no later than 6 (six) months from the day the contract goes into effect;

7. Seventh tranche-no later than 7 (seven)  months from the day the contract goes into effect;

8. Eighth tranche-no later than 8 (eight) months from the day the contract goes into effect;

9. Nineth tranche-no later than 9 (nine) months from the day the contract goes into effect;

10. Tenth tranche-no later than 10 (ten) months from the day the contract goes into effect;

11. Eleventh tranche-no later than11 (eleven) months from the day the contract goes into effect;

12. Twelvth tranche-no later than 12 (twelve)  months from the day the contract goes into effect.

The seller is obligated to deliver the contractual goods-binding elements (postions 6 an 7) of the article 3 of the Contract) to the Buyer, DDP Resavica-Central warehouse Resavica (Incoterms 2010) in the appropriate number with each delivery of steel mining support.

Buyer shall specify  in  his  order the  type and quantity of goods required, place and time of delivery.

The said text is changed and should stand as:

Seller agrees to deliver the contractual goods-steel mining support (positions 1, 2, 3, 4 and 5 of the contract)  to the Buyer , DDP Resavica- Central warehouse Resavica (Incoterms 2010), in 6 (six) equal monthly tranches  (approximately 1/6 contracted quantity for each position), as follows:

1. First tranche – no later within 30 (thirty) days from the day the contract goes into effect;

2. Second tranche-no later that 2 (two) months from the day the contract goes into effect;

3. Third tranche-no later than 3 (three) months from the day the contract goes into effect;

4. Fourtt tranche-no later than 4 (four) months from the day the contract goes into effect;

5. Fifth tranche-no later than 5 (five) months from the day the contract goes into effect;

6. Sixth tranche-no later than 6 (six) months from the day the contract goes into effect;

The seller is obligated to deliver the contractual goods-binding elements (postions 6 an 7) of the article 3 of the Contract) to the Buyer, DDP Resavica-Central warehouse Resavica (Incoterms 2010) in the appropriate number with each delivery of steel mining support.

Buyer shall specify  in  his  order the  type and quantity of goods required, place and time of delivery.

In accordance with the fore mentioned changes a revised bidding documentation has been made which will be published on the same day on the Public Procurement Portal and on the site www.jppeu.rs.

Becouse of the number of changes the date for the submision of bids will be extended. The anauncment for the extension od the submision date wil be made public on the Public Procurement Portal and on the site www.jppeu.rs.

Commission public procurement 28/15/606006